## Slide 1: Compressively sampled speech: How good is the recovery?
Kenneth V. Domingo, and Maricor N. Soriano
National Institute of Physics, University of the Philippines Diliman
SPP-2020-4C-04
22 October 2020

## Slide 2: Contents
01.
02.
03.
04.
Abstract &
Introduction
Dataset &
Methodology
Results & Discussion
Conclusions & Recommendations

## Slide 3: Abstract
Modern signal acquisition technologies are made possible by the Nyquist-Shannon sampling theorem (NST). However, this paradigm is extremely wasteful as the signal is compressed before storing it by systematically discarding imperceptible information. Compressive sensing (CS) aims to directly sense the relevant information. Current literature focus either on formulating more computationally-efficient algorithms, or methods which improve the reconstruction quality. In this paper, we quantify the reconstruction quality of compressively sampled speech with a perceptually intuitive metric—the Perceptual Evaluation of Speech Quality (PESQ)—and with the standard average segmental SNR (SNRseg). The quality of recovery of compressively sampled speech evaluated using PESQ is dependent on the compression ratio, and independent of the number of subbands used to represent the signal in the spectrogram domain.

## Slide 4: Nyquist-Shannon sampling
Real signal, continuous
Sampled signal, discrete
Reconstructed signal, continuous
fB
sampling
interpolation
Notes: Signals are sampled discretely at a fixed rate over time
Video – image snapshots at 30 images (frames) per second (fps)
Audio – amplitude snapshots at 44,100 times per second (Hz)

## Slide 5: Nyquist-Shannon sampling
Real signal, continuous
Sampled signal, discrete
Reconstructed signal, continuous
fB
sampling
interpolation
fS > 2fB

## Slide 6: Compressive sampling
Real signal, continuous
Sampled signal, discrete
Reconstructed signal, continuous
sampling
minimization

## Slide 7: Compressive sampling
Consider the linear model of signal acquisition

## Slide 8: Compressive sampling
Consider the linear model of signal acquisition
original signal
sensing matrix
sampled signal

## Slide 9: Compressive sampling
sparsifying basis
measurement basis
sensing matrix

## Slide 10: Sensing matrix constraints
Incoherence
Measurement basis should have low mutual coherence with the sparsifying basis
Sparsity
Signal must be represented in some domain where most of its coefficients are approximately zero

## Slide 11: Previously (SPP 2019)
Compressive sampling of relatively simple signals
Recorded guitar signal playing one note
One base frequency + harmonics
Error measured in terms of cosine similarity [0, 1]
Compares similarity of original & recovered frequencies, ignores magnitude

## Slide 12: Objectives
Quantify signal reconstruction error with perceptually-intuitive metrics
Compare both magnitudes and frequencies
Perform CS on complex signals (i.e., speech)

## Slide 13: Methodology
Pre-processing
Sparse transformation
Compressive sampling
Reconstruction evaluation

## Slide 14: Dataset
TIMIT Acoustic-Phonetic Continuous Speech Corpus (Garafolo et al., 1993)
Format: .WAV, 16 kHz sampling rate, 3 seconds average duration
6300 sentences (10 sentences spoken by 630 people)
File structure: <dialect-region>/<sex><speakerId>/<sentenceId>.wav
8 dialect regions corresponding to US region where the speakers grew up
  DR1: New England
  DR2: Northern
  DR3: North Midland
  DR4: South Midland
  DR5: Southern
  DR6: NYC
  DR7: Western
  DR8: Army Brat (nomadic)

## Slide 15: Dataset
Sentences consist of:
2 dialect “shibboleth” sentences (SRI)
450 phonetically-compact sentences (MIT)
1890 phonetically-diverse sentences (TI)

## Slide 16: Preprocessing
All test signals were obtained from the TIMIT Acoustic-Phonetic Continuous Speech Corpus
Format: .WAV, 16 kHz sampling rate, 3 seconds long on average
Grouped by spoken sentence, region & sex
Downsampled first to 8 kHz

## Slide 17: Sparse transformation
Images, simple audio  Fourier/frequency domain
Speech audio  modulation/spectrogram domain

## Slide 18: Sparse transformation
Define the ff:
  Length of sampling window
  Percent overlap between adjacent windows
Divide the signal into frames using a sliding window with the parameters defined above.
Multiply each frame by a window function (Hann) where is the length of the sampling window.
Take the Fourier transform of each window.

## Slide 19: Sparse transformation
The defined steps can be summarized as a short-term Fourier transform (STFT): where indicates the th signal frame, is the window function with hop size , is the time index, and is the frequency.

## Slide 20: Reconstruction evaluation
Perceptual Evaluation of Speech Quality (PESQ)
Prediction of perceived quality that would be given to a received signal by subjects in a subjective listening test
Complex series of scaling, transforming, filtering, windowing, and more
We refer to PESQ manual (ITU, 2001) for a detailed overview
PESQ value | 1 | 2 | 3 | 4 | 5
Qualitative description | bad | below average | average | good | perfect

## Slide 21: Reconstruction evaluation
Segmental signal-to-noise ratio (SNRseg) where is the frame length, is the number of frames, are the original signal samples, are the reconstructed signal samples.

## Slide 22: Results & Discussion: Representative case
Representative case: DR8/MJLN0/SA1.wav
Compression ratio = 40%, 1024 frames, 75% frame overlap
Reconstruction algorithm: LASSO where is the candidate solution, is the reconstructed signal, is the compressed signal, is the sensing matrix, is the number of compressive samples, and is the -regularization parameter.
The optimal value of is determined via 5-fold cross-validation

## Slide 23: Representative case

## Slide 24: Results & Discussion: Error maps
Error maps generated by compressively sensing the signal & evaluating the metrics for:
Compression ratio in increments of 0.1
Number of frames
Frame overlap constant at 75%

## Slide 25: Error maps

## Slide 26: Conclusions
Reconstruction quality of compressively sampled speech was quantified by compression ratio & number of frames
Evaluation of a perceptually-intuitive metric (PESQ) shows that it is sensitive only to changes in compression
Evaluation of a statistical metric (SNRseg) shows that it is sensitive only to the number of frames
Depending on the use case, the reconstruction quality of a speech signal can be described as a function solely of a relevant metric

## Slide 27: Recommendations
Test on locally-acquired speech recordings
Test on higher-sample rate signals
Test on adaptive reconstruction algorithms

## Slide 28: References
J. S. Garafolo, L. F. Lamel, W. M. Fisher, J. G. Fiscus, D. S. Pallett, N. L. Dahlgren, and V. Zue, TIMIT acoustic-phonetic continuous speech corpus LDC93S1 (Linguistic Data Consortium, 1993).
Telecommunication Standardization Sector of ITU, Perceptual Evaluation for Speech Quality (PESQ): An objective method for end-to-end speech quality assessment of narrow-band telephone networks and speech codecs, ITU-T Recommendation P.862 (02/01) (2001).

## Slide 29: Compressively sampled speech: How good is the recovery?
Kenneth V. Domingo, and Maricor N. Soriano
National Institute of Physics, University of the Philippines Diliman
SPP-2020-4C-04
22 October 2020